Model: DW-016

Microprocessor controlled wiegand format reader decoder. Provide:

- 1 wiegand reader port input;

- 2 x 16 LCD display for card number, site/facility code, bit number of read card; clock, ready sign and/or company name;

- LED indicator for each successful read;

- Micro switch to set clock (one switch to set 00:00:00 to sync clock with system);

- input voltage: 5VDC;

- watch dog protected.

Typical applications:

To check bit number, card number, site code of proximity card.

Add on real time clock for reader of ACS.

Model: DW-051

Microprocessor controlled expandable relay output board. Provide:

- 32 nos. NO/NC dry contact outputs per board;

- output connection by 2 standard 40 pins IDE flat cable (each contains 16 nos. output), easy to plug and unplug;

- each output relay paired with LED indicator for clear visual monitoring;

- build on board with system LED as heart beat and watch dog to secure stable operation;

- use RS232 interface and can be cascaded to expand to 8,192 nos. of dry contact outputs;

- output port can be changed to input port by request order;

- input voltage: 12VDC with regulated 5VDC output terminal (can use 5VDC regulated input instead of 12VDC).

Typical applications:

RS232 com port command of BMS/ACS to trigger DVR/CCTV matrix and/or other panel’s input.

Standalone automation system.

Model: DW-057

Microprocessor controlled I/O board. Provide:

- 4 wiegand reader interfaces (default 2 for IN/OUT readers and 2 for reader ports of dual reader controller board);

- 8 inputs with optical coupler protected (DC signal or can be changed to NO/NC general input);

- 4 NO/NC programmable general inputs;

- 8 dip switches initial setup for address and/or baud rate;

- 8 programmable outputs (LED indicator paired) with NC and NO terminals;

- 4 programmable voltage level outputs;

- 1 RS232 communication port;

- input voltage: 12VDC with regulated 5VDC output terminal (can use 5VDC regulated input instead of 12VDC);

- watch dog protected.

Typical applications:

Optical turnstile interface for access control system to cater anti-passback cases.

Real interlock interface to avoid delay locking of electric lock.